## Slide 1: Digital Design & Computer Arch. Lab 5 Supplement: Implementing an ALU
Prof. Onur Mutlu
ETH Zürich
Spring 2020
27 March 2020

## Slide 2: What Will We Learn?
In lab 5, you will Implement an Arithmetic Logic Unit (ALU) in Verilog and evaluate its speed and resource utilization.
Draw a block level diagram of the MIPS 32-bit ALU, based on the description in the textbook.
Implement the ALU using Verilog.
Synthesize the ALU and evaluate speed and FPGA resource utilization.

## Slide 3: Part 1: Designing an ALU
We will design an ALU that can perform a subset of the ALU operations of a full MIPS ALU.
  2 32-bit inputs
  4-bit AluOp signal to select the operation
  32-bit output
  Output flag zero that sets to logic-1 if all the bits of the result are 0.
AluOp (3:0) | Mnemonic | Result = | Description
0000 | add | A + B | Addition
0010 | sub | A - B | Subtraction
0100 | and | A and B | Logical and
0101 | or | A or B | Logical or
0110 | xor | A xor B | Exclusive or
0111 | nor | A nor B | Logical nor
1010 | slt | (A - B)[31] | Set less than
Others | n.a. | Don’t care | 

## Slide 4: Part 1: Designing an ALU- Block Diagram
First, you need to draw a block diagram of the ALU, like the one seen in Figure 5.15 of the H&H textbook.
You are free to chose if you want to draw the complete block diagram or split it up into modules and elaborate the modules, similar to the next slide.

## Slide 5: Part 1: Designing an ALU- Block Diagram
A possible division in ALU Logic and Arithmetic operations:

## Slide 6: Part 1: Designing an ALU- Block Diagram
A possible organization of ADD and SUB:

## Slide 7: Part 1: Designing an ALU- Block Diagram
A possible organization for SLT:

## Slide 8: Part 2: Implementation
Replace each block with a Verilog description.
Synthesize and implement your design.
We do not transfer the design to FPGA in this lab
  No Constraint file  Bitstream generation will fail.
At this point, we cannot verify the correctness of our circuit manually.
  You will calculate how long will the exhaustive search take.
  You learn how to use testbench to test the correctness of this circuit in lab 6! 

## Slide 9: Part 3: The performance of the circuit (I)
In this lab, we will learn to check:
  The speed (i.e., max frequency our circuit can run at)
  The area (i.e., FPGA resource utilization).
We will add a timing constraint to set the maximum delay that we would like our ALU to have.

## Slide 10: Part 3: The performance of the circuit (II)
The information we will obtain:
Number of LUTs | 
Number of bonded IOBs | 
Which pin of the FPGA is the output ‘zero’ connected? (pin name) | 
Where does the longest path start from | 
Where does the longest path end | 
How long is the longest path | 
How much of the longest path is routing | 
How many levels of logic is in the longest path | 

## Slide 11: Last Words
In lab 5, you will Implement an Arithmetic Logic Unit (ALU) in Verilog and evaluate its speed and resource utilization.
Draw a block level diagram of the MIPS 32-bit ALU, based on the description in the textbook.
Implement the ALU using Verilog.
Synthesize the ALU and evaluate speed and FPGA resource utilization.
In the report, you will use your adder from Lab 2 in the ALU and compare the resource utilization.

## Slide 12: Report Deadline
23:59, 24 April 2020

## Slide 13: Digital Design & Computer Arch. Lab 5 Supplement: Implementing an ALU
Prof. Onur Mutlu
ETH Zürich
Spring 2020
27 March 2020